## Slide 1: Wireless Channel
• Types
• Multipath analysis
• Frequency Response
• Null Formation
Rifat Bin Rashid

## Slide 2
Channel
Transmitter
Receiver

## Slide 3
© : https://www.sharetechnote.com/html/Handbook_LTE_Fading.html
Wireless Communication Channel

## Slide 4
Tx Signal
x(t)
Channel
h(t)
Noise
n(t)
Rx Signal
y(t)
y(t)=
y(t)=(x∗h)(t) + n(t)
Y(f)=H(f)X(f) + N(f)

## Slide 5
Information Source & Input Transducer
Source Encoder
Channel Encoder
Digital Modulator
Channel
Digital Demodulator
Channel Decoder
Source Decoder & Output Transducer
Source Decoder

## Slide 6
Channel Types
Large Scale Fading
Small Scale Fading
Path loss
Shadowing
Multipath delay spread
Doppler Spread
Flat Fading
Frequency Selective Fading
Fast Fading
Slow Fading
AWGN Channel
Fading Channels
Coherence Bandwidth
Coherence Time

## Slide 7
Large Scale Fading

## Slide 8
©: https://pysdr.org/content/multipath_fading.html
Multipath Fading
Impulse Response

## Slide 9
Two tap multipath
Impulse Response
h(t) = a₀·δ(t) + a₁·δ(t - τ)

## Slide 10: Channel Model Two tap multipath
Impulse Response
      h(t) = a₀·δ(t) + a₁·δ(t - τ)
Parameters:
    a₀ = Direct path amplitude (LOS)
    a₁ = Reflected path amplitude
    τ = Path delay time
    δ(t) = Dirac delta function
Rician Fading

## Slide 11: Frequency Domain
Impulse Response
h(t) = a₀·δ(t) + a₁·δ(t - τ)
Fourier Transform:
H(f) = a₀ + a₁·e^(-j2πfτ)
Complex Form:
H(f) = [a₀ + a₁·cos(2πfτ)] - j[a₁·sin(2πfτ)]
Frequency Response

## Slide 12: Magnitude Response
Complex Form:
H(f) = [a₀ + a₁·cos(2πfτ)] - j[a₁·sin(2πfτ)]
Channel Magnitude
|H(f)| = √[ (a₀ + a₁·cos(2πfτ))² + (a₁·sin(2πfτ))² ]
Simplified:
|H(f)| = √[ a₀² + a₁² + 2a₀a₁·cos(2πfτ) ]

## Slide 13: Null Formation
Fourier Transform:
H(f) = a₀ + a₁·e^(-j2πfτ)
Complete cancellation occurs when:
H(f) = 0
a₀ + a₁·e^(-j2πfτ) = 0
1 + e^(-j2πfτ) = 0
e^(-j2πfτ) = -1 = e^(-jπ)
2πfτ = π + 2πk (k = 0, 1, 2, ...)
f_null = (1 + 2k) / (2τ)

## Slide 14: Null Characteristics
Null Properties
      First Null (k=0): f₁ = 1/(2τ)
      Second Null (k=1): f₂ = 3/(2τ)
      Third Null (k=2): f₃ = 5/(2τ)
Null Spacing: Δf = 1/τ
Key Insight:
    Null spacing depends ONLY on delay τ
    Null depth depends on amplitude ratio a₁/a₀
f_null = (1 + 2k) / (2τ)